## Slide 1: Enhancing UFS Air Quality Predictions with Aircraft-Derived Regional Emission Adjustments
Youhua Tang1,2, Patrick Campbell1,2, Wei Li1,2, Barry Baker3, Kai Wang3,4, Jianping Huang3, Daniel Tong1,2, Xinrong Ren1, Eleanor Waxman5,6, Ken Aikin6, Andrew Rollins6, John Crounse7, Paul Wennberg7, Ryan Bennett8, Ilana Pollack5,6,9, Emily Lill9, Matthew Coggon6, Kelvin Bates5,6, Amy Sullivan9, Mike Robinson6, Carsten Warneke6, Lu Xu5,6, Kristen Zuraski5,6, Jeff Peischl5,6, Chris Jernigan5,6, Wyndom Chace5, Steven S. Brown6, Caroline Womack6, Gordon Novak6, Patrick Veres6, Chelsea Stockwell6, Ann Middlebrook6, Rebecca Schwantes6, Brian McDonald6, Charles Gatebe10, Youngsun Jung11
1. NOAA Air Resources Laboratory, College Park, MD.
2. George Mason University, Fairfax, VA.
3. NOAA/NCEP/EMC, College Park, MD
4. Lynker, Leesburg, VA
5. CIRES, University of Colorado, Boulder, CO
6. NOAA Chemical Sciences Laboratory, Boulder, CO
7. California Institute of Technology, Pasadena, CA
8. Bay Area Environmental Research Institute, Moffett Field, CA
9. Colorado State University, Fort Collins, CO
10. NASA Ames Research Center, MS 245-5, Moffett Field, CA
11. NOAA NWS/STI, College Park, MD

## Slide 2: Why do we need to adjust UFS model’s emission with aircraft observations?
Emissions are one of the fundamental driving forces of atmospheric composition, and their accuracy is critical for reliable atmospheric composition predictions..
To accurately represent the temporal and spatial variability of atmospheric pollutants, the current NOAA UFS-AQM requires emission adjustments to account for uncertainties and changing emission patterns.
Aircraft-based atmospheric composition measurements collected during field campaigns provide comprehensive, three-dimensional observations of numerous chemical species. These measurements are often regarded as the benchmark for model evaluation and for the calibration and validation of satellite retrieval products. Compared with surface observations alone, aircraft data offer unique insights into the vertical distribution, transport, and chemical evolution of pollutants.
Recent aircraft field experiments have generated extensive datasets
that can be used to constrain and improve emission inventories.

## Slide 3: Emission Adjustment Methods
(Lamsah et al., 2011)
where E is the targeted emission over certain regions, and C is the corresponding receptor concentrations.
2023 AEROMMA Field Campaign over CONUS

## Slide 4: Regional Emission adjustment factors for anthropogenic emissions based on the biases below 3km
 | Northern CA | Southern CA | CA Central Valley | Rockies | North Central | Northeast | Southeast | South Central
CO | 1.2 | 1 | 1.2 | 0.3 | 2 | 1.7 | 2 | 2
C2H4 | 0.7 | 2 | 0.4 | 0.8 | 0.8 | 0.5 | 1 | 1
C2H6 | 2 | 2 | 2 | 1.5 | 3 | 2.5 | 2 | 2
C2H2 | 2 | 1 | 0.5 | 1.5 | 2 | 0.8 | 2 | 2
Propane | 5 | 5 | 5 | 1.5 | 3 | 1.5 | 3 | 3
Benzene | 1.5 | 2 | 0.7 | 1 | 2 | 2 | 2 | 1
SO2 | 5 | 1 | 5 | 1 | 0.5 | 0.5 | 2 | 1
NH3 | 3 | 3 | 3 | 2 | 3 | 2.5 | 1 | 1

## Slide 5
This regional emission adjustment generally improved the predictions for emitted species compared with aircraft data

## Slide 6
Same but for C2H6

## Slide 7
Same but for SO2

## Slide 8: The improvement is also shown near surface compared to AQS data

## Slide 9: Mean daytime CO concentration changed due to the this emission adjustment, July, 2023
Mean daytime O3 concentration changed due to the this emission adjustment, July, 2023
The impact of CO and VOC emission adjustments on O3 is relatively small for summer 2023.

## Slide 10
The impact of the emission adjustments on PM2.5 is also very small for summer 2023.

## Slide 11
Southwest Marcellus
ETHA*4, CO*4
Northeast Marcellus
ETHA*2, CO*2
Great Washington/Baltimore Region ETHA*3, CO*2
Baltimore Air Quality and Marcellus Survey (BAQMS)
07/07-08/03, 2025
EmisAdj1: local CO and ethane emission adjustment
EmisAdj2: EmisAdj1 + soilnox
EmisAdj3: double CO and ethane emissions in east of Rocky mountain and North of 38N

## Slide 14
For summer 2025 (BAQMS) case, this emission adjustment help correct the ozone underpredictions.

## Slide 15: Summary
Regional emission adjustments derived from aircraft observations reflect systematic biases in emission inventories over large geographic areas. These adjustments generally improve simulations of emitted trace gases near surface including CO, ethane, ethene, and SO₂ etc, as verified by both surface and aircraft measurements across CONUS.
The local sensitivity factor (β) for long-lived species, such as CO, can exhibit substantial spatial variability, which may not be adequately represented by a constant value.
Adjustments to CO and VOC emissions have only a limited impact on ozone and PM2.5 forecasts, with the mean regional change in O₃ concentrations being approximately 1–2 ppb.